## Slide 1: What can you do with SPEC? How does it work?
Alex Grasman
Martin van Hees

## Slide 2: Agenda
Background
Overview
Demonstration

## Slide 3: Why did MARIN develop SPEC?
Develop our own knowledge
Apply knowledge in the public domain
Support the shipping sector: What will be the energy carrier(s) of the future?
Support ship owners:
  How will ship designs be affected
  How do we prepare for 2030 / 2050 emission targets?

## Slide 4: What is SPEC?
Collection of energy carriers and systems from publications and symposia
Compare and rank solutions based on multi-criteria
Previously Excel based
Online Database: https://sustainablepower.application.marin.nl
Quaestor platform
Dedicated studies performed in several projects to date
Knowledge utilised in many more projects
Notes: Explain the data knowledge collection from papers and symposia. Comparison tool.

## Slide 5: What are the system boundaries in SPEC
Any Generator
Electrical storage
Energy
storage
Pre-treatment and distribution
Ships power and propulsion
Any Generator
VAC
VDC
Consumers
Ships pay load consumers
Consumers
Consumers
Shore grid
After treatment
Emissions
Power
Ships services
Ships services
Gearbox
Internal Comb Engine
Energy carrier
Consumers
SPEC building blocks in mass-to-power flow:
Energy storage
Pre-treatment
Energy conversion
Power distribution, converters and drives
After treatment
Energy carrier
M/G
Notes: A hybrid configuration is also what MARIN’s ZEL will feature
It allows for different power sources and conversion methods to be used, independently or together:
  Auxiliary gensets
  Electrical storage
  Main propulsion engine
Bi-directional tap on gearbox can increase shaft power delivered by diesel (‘boost’) or power the shaft on its own (source is genset or electrical storage), but the other way also works: increase loading of a diesel at lower speeds, to deliver hotel loads or charge a battery bank

## Slide 6: What does SPEC do?
Stored energy
Power systems
Contained energy density
Pre-treatment
Power distribution & drive
Energy to power
After-treatment
Electric distribution
Gear boxes and shafts
Emission information
Properties:
Energy/Power density
CapEx
OpEx
Efficiency
TRL
Notes: Conversion from energy carrier to power
  In this step the type of conversion from carrier to physical power is made. F.e. by Internal Combustion Engine (ICE) [bkW] or Fuel Cell [ekW]. Some of the carriers have multiple possibilities. F.e. methanol can be burned in an ICE, but from methanol separated hydrogen (called ‘dehydrogenation’) can also be processed in a fuel cell.
Energy carrier pre-treatment
  Some energy carriers do not have the right appearance for power conversion. What type of physical or chemical conversion must be applied depends on the type of power conversion
  F.e. 250 bar compressed natural gas has expand to 5-10 bar for streaming into the air inlet system of an ICE.
Exhaust after treatment
  ICE conversions sometimes require after treatment as per IMO Tier III or EU Stage V. This will prevent exhaust gasses to emit (excessive) amounts of harmful substances, like NOx and Particulate Matter

## Slide 7: What does SPEC do?
Stored energy
Power systems
Contained energy density
Pre-treatment
Power distribution & drive
Energy to power
After-treatment
Electric distribution
Gear boxes and shafts
Emission information
Properties:
Energy/Power density
CapEx
OpEx
Efficiency
TRL
???
AND
Notes: Conversion from energy carrier to power
  In this step the type of conversion from carrier to physical power is made. F.e. by Internal Combustion Engine (ICE) [bkW] or Fuel Cell [ekW]. Some of the carriers have multiple possibilities. F.e. methanol can be burned in an ICE, but from methanol separated hydrogen (called ‘dehydrogenation’) can also be processed in a fuel cell.
Energy carrier pre-treatment
  Some energy carriers do not have the right appearance for power conversion. What type of physical or chemical conversion must be applied depends on the type of power conversion
  F.e. 250 bar compressed natural gas has expand to 5-10 bar for streaming into the air inlet system of an ICE.
Exhaust after treatment
  ICE conversions sometimes require after treatment as per IMO Tier III or EU Stage V. This will prevent exhaust gasses to emit (excessive) amounts of harmful substances, like NOx and Particulate Matter

## Slide 8: Energy carriers and their characteristics
992 records of energy carrier properties
to date

## Slide 9: Energy carriers and their characteristics
Contained energy density is incl. weight/volume of storage medium
WTT, Well-to-Tank emission from the energy carrier production and distribution
Energy carrier CapEx are captial expenses for energy carrier storage
TRL = Technical Readiness Level of the energy carrier storage

## Slide 10: Solutions: Ship Power and Energy System
= Energy storage + Pre-treatment + Energy conversion + After-treatment + Distribution
WTW = Well-to-Wake: emissions from production and the ship itself
Emissions given per unit of energy delivered by the system to the consumers

## Slide 11: Example: Heavy Lift Vessel
Average power = 45%
Installed = 22 MW
Autonomy = 700 hours

## Slide 13: Using SPEC: Preselection of system concepts

## Slide 14: Using SPEC: Preselection of system concepts
List of compliant solutions from 43 energy system concepts

## Slide 15: Using SPEC: Ranking of system concepts

## Slide 16: Using SPEC: Ranking of system concepts

## Slide 17: Using SPEC: Ranking of system concepts

## Slide 18: Effect analysis: TCO versus CO2 emission rights

## Slide 19: Effect analysis: Ranking technology and investment

## Slide 20: Effect analysis: Operations ranking

## Slide 21: Effect analysis: Overall ranking

## Slide 22: Using SPEC: Design cases
Design cases:
  Impact of system concept op main particulars, payload, speed, power etc.
  Tuning of parameters with benchmark vessels
  Input independent from Pre-selection
  Input in different forms, ratios, dimensions, installed power, speed…
  Lifespan, downtime, power profile, endurance

## Slide 23: Using SPEC: Design cases
Three main design cases:
  Speed fixed with three variants
  Power fixed with three variants
  Speed free with two variants
In total 8 design cases with combinations
  Speed
  Power
  Payload
  Displacement
  Dimensions

## Slide 24: Using SPEC: Design cases, variation of system concept

## Slide 25: Using SPEC: Design cases, variation of system concept

## Slide 26: Using SPEC: Design cases, variation of endurance

## Slide 27: Using SPEC: Design cases, variation of endurance

## Slide 28: Summary
SPEC is a conceptual design tool that can assess the performance of energy- and power systems, based on the ship design and its mission (endurance, payload, etc..);
Do you want to find out what alternative energy- and power systems are suitable for your ship?
And how the ship design and operations will be affected?
Get in touch: a.grasman@marin.nl
Our database (in development) can be found here: http://sustainablepower.application.marin.nl (we are open to suggestions for data improvement!)